## Slide 1: ZeroTrustLAN Project
Implementing Zero Trust Architecture
Cisco Packet Tracer Simulation

## Slide 2: Team Members
Shahd Abdelfattah
230100513
Hagar Maher
230105968
Mohamed Amr
230101033
Ahmed Mohamed
230100126
Mohamed Salah
230104466

## Slide 3: TABLE OF CONTENTS Introduction to Zero Trust Architecture ZeroTrustLAN Project Purpose 01 03 02 04
Network Topology and Devices
Implementation Steps
Testing and Validation
05
06
Conclusion and Future
Enhancements

## Slide 4: INTRODUCTION
to Zero Trust Architecture

## Slide 5: What is Zero Trust Architecture (ZTA)?
Core Principle: "Never Trust, Always Verify"
Key Features:
Micro-segmentation: Isolate network segments
Least Privilege: Minimal access permissions
Continuous Identity Verification
Relevance: Protects fintech networks from threats

## Slide 6: Why ZeroTrustLAN?
Simulate ZTA for a fintech firm
Benefits:
Enforce strict access control
Limit lateral threat movement
Validate device identity via MAC addresses
Tools:
Cisco Packet Tracer, Layer 3 switches, VLANs

## Slide 7: Network Topology ZeroTrustLAN Topology Devices VLANs
2 Cisco 3560 Layer 2 Switches (SW1, SW2)
11 PCs (10 authorized, 1 unauthorized: PC_UNAUTH)
VLAN 10: Admission
VLAN 20: HR
VLAN 30: Labs
VLAN 40 : Admin
Trunk Link: SW1 Fa0/24 ↔ SW2 Fa0/24

## Slide 8: VLAN 10 (Admission) VLAN 20 (HR) VLAN 30 (Labs)
Ports Fa0/1–3 on SW1
Ports Fa0/1–4 on SW2
Ports Fa0/11–13 on SW1
VLAN 40
(Admin)
Added for monitoring
Trunk link between SW1 and SW2 on Fa0/24

## Slide 9: VLAN Configuration
  SW1 Configuration:
    VLAN 10 (Admission): Fa0/1–3
    VLAN 20 (HR): Fa0/11–13
    Trunk: Fa0/24
  SW2 Configuration:
    VLAN 30 (Labs): Fa0/1–4
    Trunk: Fa0/24
  Key Commands:
    switchport mode access
    switchport mode trunk
  VLAN and Trunk Setup

## Slide 10: Port Security Configuration
  Features:
switchport port-security maximum 1 – Allows only one MAC per port
switchport port-security mac-address <MAC> – Binds specific MAC address
switchport port-security violation shutdown – Disables port on violation
  Example:
  SW1 Fa0/1 allows only PC_ADM1
  Outcome:
  PC_UNAUTH triggers shutdown when plugged into unauthorized port

## Slide 11
Access Control Lists
(ACLs)

## Slide 12
ACL Rules:
Each VLAN has a dedicated ACL (e.g., VLAN10_ACL)
Allows gateway access only within same VLAN
Denies all other intra-/inter-VLAN traffic
Example Command:
ip access-list extended VLAN 10_ACL

## Slide 13: Secure Management (AAA/SSH)
  SW1 Configuration:
Admin access restricted to VLANs 10 and 20 only
AAA used for authentication (username: admin)
VTY lines protected with access-lists
SSH configured with domain and RSA keys

## Slide 14: Testing - Identity Validation Test Case: PC_UNAUTH connected to Fa0/1 or Fa0/11 will cause port shutdown (err-disabled) Use: show port-security interface fa0/1 to verify
Verification:
Authorized devices connect normally
Authorized PCs connect successfully

## Slide 15: SDN Integration & Python API Script Content:
SDN Controller added in VLAN 40 for monitoring
Cisco Network Controller provides device visibility
Python script uses REST API to retrieve host info (MAC, IP, Hostname, Interface)
Script handles authentication and parses JSON data

## Slide 16: Testing - VLAN Communication Intra-VLAN: PC_ADM1 pings PC_ADM2: Succeeds PC_HR1 pings PC_HR2: Succeeds Inter-VLAN: PC_ADM1 pings PC_HR1: Fails (ACL enforced) Gateway Ping: All PCs reach their SVI

## Slide 17: Testing - Management Access SSH Test: SSH from PC_ADM1 (VLAN 10) to SW1: Succeeds SSH from PC_HR1 (VLAN 20) to SW1: Succeeds SSH from PC_LAB1 (VLAN 30) to SW1: Fails SSH from PC_LAB1 to SW2: Succeeds

## Slide 18: Conclusion
Achievements:
VLAN segmentation for micro-segmentation
Port Security for identity verification
ACLs for least privilege
Secure management with AAA/SSH
Outcome:
Robust defense against unauthorized access

## Slide 19: THANK YOU! Does anyone have any questions?
Future Enhancements:
Implement 802.1X authentication with RADIUS
Enable DHCP Snooping & Dynamic ARP Inspection
Integrate a firewall for inter-VLAN filtering